## Slide 1: Partitioning (continued)

## Slide 2
Fiduccia-Mattheyses (FM) Algorithm
•Modified version of KL
•A single vertex is moved across the cut in a single move
–Unbalanced partitions
•Vertices are weighted
•Concept of cutsize extended to hypergraphs
•Special data structure to improve time complexity
–(Main feature)
•Can be extended to multi-way partitioning

## Slide 6
Each pointer in the array list A (or B) points to a linear list of unlocked vertices inside A (or B) with the corresponding gain

## Slide 7
The FM Algorithm: Balanced Partition
•Definition. A maximum vertex weight W which satisfies the relation W >w(V)/2 + maxvεV{w(v)},
where w(v) = weight of vertex v,
w(V) = sum of the weights of all vertices
•Balanced partition {A|B} is one having a total vertex weight of at most W, i.e., w(A), w(B) <W.

## Slide 9
An initial balanced partition can be obtained by sorting vertex weights in decreasing order, and placing them in A and B alternatively

## Slide 12
FM Algorithm: Time complexity
Data structures list A and B are initialized by traversing all hyperedges one by one
Consider the hyperedge ea={M1,M2,…..,Md}, when e1, e2, e3,……,ea-1 are already visited
Let num(A) is the no of modules connected by ea that are in A.
If num(A)=0, then gain of each module Mi in {M1,M2,…..,Md} is decreased by w(ea).
If num(A)=1, the gain of one module Mi in {M1,M2,…..,Md} that is in A is increased by w(ea ).
If num(A)>1, no action takes place unless num(B)= 0 or num(B)=1.
The same analysis holds for num(B).
Time spent for processing ea is O(d). d= the total number of terminals (t)
Finding the modules with maximum gain in list A and list B takes a constant time, if this value is maintained and updated while processing ea.
Thus the time complexity of building data structures list A and list B is O(t+n), where n = the number of modules

## Slide 13
FM Algorithm: Time complexity
In one pass, find a module with maximum gain using doubly linked pointers
Let a module Mi (in hyperedge ea) is in A and is moved to B
Case 1: if all modules of ea are in A (before moving Mi), the gain of all these modules will be increased by w(ea).
Case 2: if all modules of ea are in B (right after moving Mi), the gain of all these modules will be decreased by w(ea).
Time taken to update the gain in each case is O(da), where da is the number of modules connected to ea
Since each hyperedge will be considered twice (case 1 and 2), it takes time proportional to number of terminals to update the list
Total time is O(ct), where c= the number of passes (independent of t)

## Slide 15
Partitioning using Replication

## Slide 19
Partitioning and Delay Problem
If a critical path is cut many times by the partition, the delay on the path may be too large to meet the goals of the high performance systems
The design of a high performance system requires partitioning algorithms to reduce the cut size as well as to minimize the delay in critical paths

## Slide 22
The on-board delay is three orders of magnitude larger than on-chip delay